## Slide 1: Smart Battery Charger
For you and for the world
Team members:
Anna Geraci
Carlo Simone
Fabio Gianino
Michele Petrocelli

## Slide 2: General information about Smart Battery Charger application
Objective:
Electric vehicles are going to dominate the transport sector in the near future, but at the same time, currently, the power used to charge them is mostly produced by burning fossil fuels. This will lead to an unsustainable scenario if actions are not taken to smoothen the transition towards electric vehicles. Under the outlined point of view, this report presents a solution that has the potential to mitigate the inconveniences related to a massive diffusion of electric vehicles, that are overloading the grid power demand, long charging times, etc..
Main characteristics:
- remote control of appliances.
- control strategies to minimise energy cost.
- end-user application for energy-awareness.
- end-user application for battery autonomy.
- unified interfaces (i.e. REST Web Services and MQTT queues) available to enable Demand/Response.
Stakeholders:
Smart Automotive, Smart grid, Smart Building
IMMAGINE

## Slide 3: Communication paradigms used
REST:
How it works
MQTT How it works

## Slide 4: Use Case Diagram - proposal

## Slide 5: Use Case Diagram - update

## Slide 6: Catalog
The Catalog has:
General Information:
User List:
Device List:

## Slide 7: GET method

## Slide 8: POST method

## Slide 9: PUT method

## Slide 10: Update the DeviceList

## Slide 11: Device Connectors

## Slide 12: Battery Charger System Control
Communication with:
Sensors: Retrieves data from sensors and process them.
Actuator: Sends command to the actuator (On/Off).
User: Retrieves data about what the user want through User Awareness interface (Node-red and Telegram - ManualFlag).
Catalog: Retrieves data of the user and general data of the application; and publish the value of the actuator computed.
Control Strategy Agenda: Retrieves the value of the percentage of battery necessary in this day according to the Agenda of the user.
Main role:
Retrieve data and choose if the car must be in charge or not according to the logic reported on the right.

## Slide 13: Agenda Control Strategy Compute the percentage of battery necessary to the specific user each day, according to the Agenda information.
Communication with:
Catalog: to retrieve information about user’s battery characteristics and user’s Agenda.
StateControl: to send AlertSMS, in case it may be necessary.
Actuator Control Strategy: to send information about the percentage of battery needed by the user in this specific day.
Main role:
Compute the percentage of battery necessary for the users during this day, according to the battery characteristics and the personal commitments.

## Slide 14: State Control
Communication with:
Sensors: to retrieve information about the status of the battery and general information.
TelegramBot: to send AlertSMS, in case it may be necessary.
Agenda Control Strategy: to retrieve information in case the number of kilometers is too high for a single recharge cycle.
Main role:
Compute the percentage of battery necessary for the users during this day, according to the battery characteristics and the personal commitments.
Vehicle present in charge station
Temperature of the battery.
Percentage of battery too low
Km necessary more than autonomy

## Slide 15: Data Analisys & ThingSpeak

## Slide 16: Node-red
Communication via MQTT with:
Sensors: to retrieve the information that they detect.
Actuator Control Strategy: to send information about value of the flag about the manual actuation.
Main Role:
Visualize data come from sensors and allow the user to set the Charger On or Off manually, through 3 buttons that sends MQTT messages to the topic related to the manualFlag.
IMMAGINE DASHBOARD FUNZIONANTE

## Slide 17: Telegram Bot
Command:
/start: Show to the user all the command available on TelegramBot.
/IsPresence: Communicate to the user if the vehicle is in charge station or not.
/AlertSMS: Communicate to the user if there are issue about the charging of his vehicle.
All this commands shows to the user the information that he requests, through text.
Each user registered his Telegram Profile through the ChatID in the Catalog, if your profile is not registered the bot tell you that you do not have the permition.

## Slide 18: Telegram Bot
/Agenda*day*: Show to the user the Agenda saved in the catalog according with the *day* specified.
/Agenda*day*Update: Allow the user to add to the Agenda a new commitments in this specific *day*
/ViewGraphs: Show to the user all the graph about the sensors and use of the application.

## Slide 19: Telegram Bot
/switch: Allow the user to choose the charge status of the car.
/exit: Allow the user to exit from any request
You can continuosly send a charger actuation, until you don’t send another command or send /exit